## Slide 1: PPT WIND SCHOOL (CLASS 14b) Engineering

## Slide 2: outline
Introduction
Engineering
  Site Layout
  Interconnection
    One Line
  Impact on Siting
  Consideration during Development

## Slide 3: introduction
Engineering is the backbone of any project
Includes the following:
  Safety Planning
  Optimization
  Client’s Goals
All engineering flows through OE
  In-house staff
  Close partners
Engineering for success before the project begins

## Slide 4
Engineering
Existing Conditions

## Slide 5
Goal is to optimize production but save construction costs
Have to consider construction costs
  Labor
  Materials
    Rock
    Collection Line
    Trees
  Equipment needed
Utilizing/Avoiding terrain and existing infrastructure
Engineering
Impact on Siting

## Slide 6
Roads
  Boring or overhead implications = $$$
Steam/River
  Boring or overhead implications = $$$
Forest
  Removal of trees = Time
Elevation changes
  Resulting in flooding
  Implications on drainage
Engineering
Considerations During Development

## Slide 7
What is needed
  Access Drives
  Crane Pads
  Parking and Laydown Yard
  Collection Lines
  Communication Lines
  Crane Staging Area
  Turbine Components Staging Area
  Drainage
Engineering
Site Layout

## Slide 8
Where would you place collection lines and access roads?

## Slide 9
Engineering
Site Layout

## Slide 10
Engineering
Site Layout

## Slide 11
Engineering
Collection Line

## Slide 12
Engineering
Collection Line
How will the collection line cross the road?
Bore
Overhead

## Slide 13
Bore Layout

## Slide 14
Representation of complicated electrical distribution system into a simplified description.
Main components are indicated by standard graphical symbol
Provides information how the components connect and how the power flows through the system.
  Flow of electricity from turbines to customer
Engineering
One-Line

## Slide 15
Engineering
One-Line

## Slide 16
Engineering
One-Line: Turbine and Transformer

## Slide 17
Engineering
Permanent Magnet Direct Drive Generator

## Slide 18
Engineering
AC Three Phase (3Φ) - Power (Watts) = Volts x Amps

## Slide 19
Engineering
One-Line: Generator to Basement
Generator
Gen to Nacelle
To Transformer

## Slide 20
Engineering
One-Line: Step-Up Transformer
High Side - Grid
Low Side - Turbine

## Slide 21
Engineering
One-Line: Ground Transformer & Switchgear

## Slide 22
Engineering
One-Line: Switchgear

## Slide 23
Engineering
One-Line: Point of Common Coupling

## Slide 24
Engineering
Geotech
Completed after a project has been signed and land/easement is obtained
To explore and evaluate the subsurface conditions at the proposed WTG sites, develop geotechnical design and construction recommendations for the project
Implications on foundation design, grounding grid, and existing conditions. Used to calculate ground bearing pressure for crane pad and for backfilling foundation.

## Slide 25
Engineering
Geotech
Analyzes allowable bearing pressure and water table

## Slide 26
Engineering
Geotech

## Slide 27
Engineering
Geotech
Analyzes minimum soil resistivity – structure & grounding

## Slide 28
Engineering
Geotech
Multi-Channel Analysis of Surface Waves
  Evaluate engineering and Geotech properties (stiffness) of subsurface

## Slide 29
Engineering
Why is it so Important?
Wind Energy engineering encompasses many fields
  Aerospace Engineer
    Creating turbine blades and rotors
  Civil
    Design support structures for turbines and related infrastructure
  Electrical
    Create and test electronic components of turbines involved in creating electricity
  Electronics
    Work on systems that use electricity to operate the turbine
  Environmental
    Assess and minimize potential environmental impacts
  Industrial
    Plan and supervise manufacture of wind turbines
  Materials
    Research, create, and test materials involved in operating turbines
  Mechanical
    Design, develop, and test machines involving in operating turbines.
  Network
    Communication and security involving operating turbines.

## Slide 30
Engineering
Why is it so Important?
Vertical Integration
  Wind Energy is complicated but a project with One Energy is not.

## Slide 31: Questions?
Questions? Comments? Concerns?
Report Writing
Next class:

## Slide 32
Electrons Move From Atom To Atom
Current: Flow of electrons
  Units: Amperes or Amps
Voltage: Electrical “pressure” or “potential” [“Potential difference”]
  Units: Volts
Engineering
Electricity

## Slide 33
Engineering
“Power Wheel”

## Slide 34
Direct Current (DC)
  Thomas Edison
  Low voltage (~100 volts) systems
  Distributed generation
Alternating Current (AC)
  Nikola Tesla and George Westinghouse
  Allows high voltage generation
  Easy conversion higher-to-lower or lower-to-higher voltage with transformer
  Transmission much more efficient
Engineering
War of Currents – Late 1800s

## Slide 35
Engineering
Electricity

## Slide 36
Engineering
AC Single Phase (1Φ)
60 Hertz = 60 Cycles per Second

## Slide 37
Engineering
AC Three Phase (3Φ)

## Slide 38
Engineering
AC Three Phase (3Φ)

## Slide 39
Line-to-Line (Phase-to-Phase) = √3 x Line-to-Ground
(√3 = 1.732)
Engineering
AC Three Phase (3Φ)
 | Line-to-Line | Line-to-Ground
Harpster | 4160 | 2400
Whirlpool, Haviland, Cooper Farms | 12470 | 7200
Ball | 34500 | 20000

## Slide 40
Engineering
AC Single Phase (1Φ) or AC Three Phase (3Φ)

## Slide 41
Engineering
AC Single Phase (1Φ) - Power (Watts) = Volts x Amps

## Slide 42
Engineering
AC Three Phase (3Φ) - Power (Watts) = Volts x Amps

## Slide 43
Engineering
Permanent Magnet Direct Drive Generator

## Slide 44
Three Phase AC Power
Three separate conductors, each with Voltage and Current shifted by 120° relative to each other
Voltage
  Line-to-Ground
  Line-to-line (phase-to-phase) = √3 x Line-to-Ground
Current
  Current in each phase = total current / √3
Power = V x A
  Power in each phase varies
  Total power is constant
Engineering
AC Three Phase (3Φ) Summary

## Slide 45
Engineering
Transformers

## Slide 46
E2 / E1 = N2 / N1
OR
E2 = E1*N2 / N1
If E1=4160V; N2=100; N1=1733; I1=15A
Find E2: E2 = 4160V*100/1733 = 240V
Engineering
Transformers

## Slide 47
I2 / I1 = N2 / N1
OR
I2 = I1*N2 / N1
Find I2:
I2 = 15A*1733/100 = 260A
Engineering
Transformers

## Slide 48
Find Power = V x A = Watts
P1 = 4160V x 15A = 62,400 Watts
P2 = 240V x 260° = 62,400 Watts
Engineering
Transformers