## Slide 1: PPT Wind school (class 16) FAA process

## Slide 2: Outline
Background
The FAA Filing Process
14 CFR Part 77 Definitions
ODOT Process
Comparison of Surfaces
Existing Structures in OH
Examples

## Slide 3: background
Title 14 of the Code of Federal Regulations (CFR) is entitled Aeronautics and Space
  Also known as the Federal Aviation Regulations
14 CFR Part 77: Safe, Efficient Use, and Preservation of the Navigable Airspace
  (c) The process for aeronautical studies of obstructions to air navigation or navigational facilities to determine the effect on the safe and efficient use of navigable airspace, air navigation facilities or equipment; and

## Slide 4: background
14 CFR Part 77 and the FAA
Part 77 allows the FAA to:
  Evaluate
    The effect of proposed construction or alteration on safety in air commerce
    The efficient use and preservation of the navigable airspace of the airport traffic capacity at the public use airports
  Determine
    Whether a proposed construction or alteration a HAZARD to air navigation
    Determine appropriate marking and lighting recommendations, using FAA Advisory Circular 70/7460-1, Obstruction Marking and Lighting
    Other appropriate measures to be applied for continued safety of air navigation
  Notify
    The aviation community of construction or alteration of objects that affect navigable airspace, including revision of aeronautical charts

## Slide 5: Faa filing process
Step 1: Notice Criteria
“Notice Criteria”: when you need to file a new construction or alteration with the FAA (https://oeaaa.faa.gov/oeaaa/external/gisTools/gisAction.jsp?action=showNoNoticeRequiredToolForm)
  If you propose any construction or alteration described in §77.9, you must provide adequate notice to the FAA of that construction or alteration.
  200 Feet above ground level
  In excess of established notification standards (lower heights, closer to an airport)
  Must file a “7460-1” 45 days prior to construction

## Slide 6: Faa filing process
A specialist from the Obstruction Evaluation Group will be assigned to the project
  The specialist acts as the “Judge”, who's job it is to collect all of the necessary information and rule impartially
  Usually a former Air Traffic Controller
Technicians from 10 groups will review each point to ensure the proposed project does not interfere with their areas of responsibility
The specialist compiles the comments from all 10 groups
Step 2: Initial Review

## Slide 7: Faa filing process
The specialist consults at least 10 groups including:
  Airports
  Instrument Flight Procedures Impact Team
  Flight Standards
  Technical Operations
  Frequency Management
  Air Force
  Navy
  Army
  Department of Defense Siting Clearing House
  Department of Homeland Security
Step 2: Initial Review Cont’d.
Hundreds of people within the FAA are involved in a filing.
Within the FAA
Outside the FAA

## Slide 8: Faa filing process
DEFINITIONS:
  Obstruction To Air Navigation: Any object the FAA determined must be properly marked, lighted, and identified on aeronautical publications so it may be easily recognized by aircraft navigating through the airspace.
  Hazard to Air Navigation: An obstruction or other adverse object that FAA aeronautical study concludes would have a “substantial adverse effect” to a “significant volume of aeronautical operations.”
Step 3: Preliminary Results

## Slide 9: Faa filing process
The Specialist will issue either:
  Determination of No Hazard
  Notice of Presumed Hazard
This is based on the results from each of the 10 departments
A “Notice of Presumed Hazard” means the FAA has identified a potential issue and the project will require further study (an Aeronautical Study) to determine if the project will pose a hazard to air navigation
Usually, all “obstructions” are initially issued a Notice of Presumed Hazard (14 CFR Part 77.17: Obstruction Standards)
  Not all obstructions are hazards…
Step 3: Preliminary Results Cont’d.

## Slide 10: Faa filing process
Step 4: Further Study
If the project owner agrees, the project will be “circularized” for public comment
During this 37 day public comment period, the FAA can collect information regarding the actual impact on the local flying community including:
  The airport
  The pilots
  Local aviation groups
    Private Jets
    Regional Airlines Association
    National Business Aviation Association
    Other lobbying groups
They will also conduct a deeper study into the potential issue:
  Technical Operations Detailed Study (VOR)
Big question: the project has an affect on air navigation, but is it significant? Is the obstruction a hazard to safe air navigation?

## Slide 11: Faa filing process
The Specialist will issue either:
  Determination of No Hazard to Air Navigation
    “The aeronautical study revealed that the structure would have no substantial adverse effect on the safe and efficient utilization of the navigable airspace by aircraft or on the operation of the air navigation facilities.”
  Determination Of Hazard to Air Navigation
The letter issued will include the comments the FAA received during the public circularization period and their responses to those comments (if any)
Step 5: Final Determination

## Slide 12: 14 CFR Part 77 Definitions
Notification Criteria
Obstruction Standards
Imaginary Surfaces
… These are all very different

## Slide 13: 14 CFR Part 77 Definitions
Notification Requirements
100:1 or 50:1
20,000 ft
10,000 ft
Runway
200 ft AGL
*Image not to scale
On Airport
= Must File 7460-1 with FAA at least 45 days prior to construction
100:1 or 50:1
Does not Require Filing
Requires Filing

## Slide 14: 14 CFR Part 77 Definitions
Obstruction Standards 77.17 (A)(1)/(A)(2)
200 ft AGL
499 ft AGL
3 NM (18,228 ft)
4 NM (24,304 ft)
5 NM (30,380 ft)
300 ft AGL
400 ft AGL
300 ft AGL
400 ft AGL
499 ft AGL
200 ft AGL
Part 77.17(a)(2) Obstruction Standards
ORC 6 Imaginary Surfaces
10,000 ft
150 ft AGL
4,000 ft
6 NM (36,456 ft)
Part 77.17(a)(1) Obstruction Standards

## Slide 15: 14 CFR Part 77 Definitions
77.19 Imaginary Surfaces
14 CFR Part 77.19 Imaginary Surfaces
Horizontal Surface
  5,000 or 10,000 ft from airport depending on runway type
Conical Surface
  4,000 feet past the horizontal surface
Primary Surface
  200-1000 ft depending on runway type
Approach Surface
  Width: 1,250 ft – 16,000 ft depending on runway type
  Distance:
    5,000 – 10,000 for non precision instrument runways
    50,000 for precision instrument runways
Transitional Surface
  Connects the primary, approach, and conical surfaces at a slope of 7:1.
Referenced in the Ohio Revised Code

## Slide 16: 14 CFR Part 77 Definitions
Imaginary Surfaces

## Slide 17: 14 CFR Part 77 Definitions
OCR 6 Imaginary Surfaces + 14 CFR Part 77.17(a)(2)
Imaginary Surfaces with 77.17(A)(2)

## Slide 18: 14 CFR Part 77 Definitions
VFR Traffic Patterns
Visual Flight Rules: regulations under which a pilot operates an aircraft in weather conditions generally clear enough to allow the pilot to see where the aircraft is going
Traffic Pattern: standard path for coordinating air traffic. Allows pilots to know from where to expect other air traffic.
Category: A-D
D
C
B
A

## Slide 19: 14 CFR Part 77 Definitions
VFR Categories
19
Category A: <91 knots
Small single engine airplanes
Category B: 91 – 120 knots
Commuter aircraft, business jets
Category C: 121 – 140 knots
Medium range commercial planes
Category D: 141 – 165 knots
Heavy Range commercial and heavy transport
VFR Traffic Patterns Vary based on the runway design and the allowable approach speeds for safe landing. Aircraft are categorized by approach speed:

## Slide 20: ODOT Process
ODOT automatically retrieves filings from FAA system.
The ORC gives ODOT authority to issue/deny a permit within the 6 imaginary surfaces. (See 4561.31(a))
However, ODOT has recently taken the position that all obstructions under Part 77 should be denied permits.

## Slide 21: ODOT Process
1 - 2 people within ODOT and one outside consultant that handle all airspace evaluation matters (compared to hundreds at the FAA)
  ODOT usually no prior experience in airspace matters
  Consultant only screens for Part 77.17 (a)(1)/(a)(2) obstructions
Only one group within ODOT (compared to 10 at the FAA)
ODOT has then the position that it will deny permits for any structure that penetrates any Part 77 surface
Does not conduct an “Aeronautical Study”
Obstructions = Hazards

## Slide 22: Comparison of surfaces
Findlay Airport
Key | Farthest Point | Distance | Square Miles
 | ORC 6 Imaginary Surfaces | 3 miles | 28 miles2
 | Part 77.17 (a)(2) Obstruction Standard | 7 miles | 150 miles2
*Height restrictions vary within the areas.

## Slide 23: Comparison of surfaces
What about all of OH?
ODOT Permit Requirement | Square Miles | % of Ohio*
Current ODOT ORC Permit Area: 6 Imaginary Surfaces | 3,950 miles2 | ~10%
Proposed ODOT Permit area: 14 CFR Part 77.17 (a)(2) | 19,107 miles2 | ~40%
Proposed ODOT Permit area: 14 CFR Part 77.17(a)(1) (>499 ft) | 44,825 miles2 | 100%
*Does not exclude overlapping surfaces, assuming mid-size airports

## Slide 24: Comparison of surfaces
Imaginary Surfaces
ORC 6 Imaginary Surfaces
3,900 mi2
9.5% of Ohio

## Slide 25: Comparison of surfaces
Part 77.17(A)(2) Surfaces
Part 77.17(a)(2)
>19,000 mi2
46% of Ohio

## Slide 26: Comparison of surfaces
Part 77.17(A)(1) Surfaces
Part 77.17(a)(1)
44,825 mi2
100% of Ohio
Everything over 499 ft

## Slide 27: Existing structures in oh
Structures existing in Ohio that violate the (a)(2) surface of airports

## Slide 28: Existing structures in oh
Structures existing in Ohio that violate the (a)(1) surface (>499 feet)

## Slide 29: Examples
Ottawa, Ohio turbine
  >16,900 feet from Putnam County Airport
  Exceeds Part 77.17 (a)(2) by 167 ft
  Received a “Notice of Presumed Hazard” from the FAA
    It was classified as an “obstruction” that needed further study
  Aeronautical study was conducted and public comment period was opened
  Conclusion: Determination of No Hazard to Air Navigation
1. Ottawa, OH

## Slide 30: examples
1. Ottawa, OH, cont’d
FAA: Determination of No Hazard
ODOT: Denial
Obstruction = Hazard

## Slide 31: examples
1. Ottawa, OH, cont’d
ODOT: Denial
Penetrates Part 77.17(a)(2) surface

## Slide 32: Examples
2. Findlay, OH
Findlay, Ohio Turbine
  >24,000 ft to Findlay Airport
  Exceeds 77.17(a)(2) as applied to a visual approach runway by 57 feet (Category D Airpsace)
  Received a “Notice of Presumed Hazard” from the FAA
    It was classified as an “obstruction” that needed further study
  Aeronautical study was conducted and public comment period was opened
    The Aeronautical Study concluded Category D aircraft do not use the aircraft at least once per day
  Conclusion: Determination of No Hazard to Air Navigation

## Slide 33: Impact to Projects
The FAA can take 60 days, 90 days, 180 days+ to respond to a Notice of Proposed Construction, depending on how busy they are
If multiple departments (like the DoD) need to weigh in, it can take longer
Filing as early as possible for our projects is important so the FAA doesn’t hold up the process
We can’t file for locations on land the customer owns unless we have permission
We CAN file for locations on land that we would have to purchase for the project without permission
Head of PPT’s decision on when to file
When to File

## Slide 34: How to FIle
https://oeaaa.faa.gov/oeaaa/external/portal.jsp
Login to our account: filings@oneenergyllc.com
“Add new case (off airport)”
  Notice of: Construction
  Duration: pick a long time period or leave blank
  Work Schedule: leave blank
  State filing: leave blank
  Structure height: 410 feet
  Requested marking/lighting: white pant/synchronous red lights
  Description of land: “Agricultural/undeveloped land outside/near ______”
  Description of proposal: “Private wind turbine.”
  Structure type: Wind turbine
  Structure name: XX-WTG## …where “XX” is the first letter(s) of the company and ## is the turbine number
  Don’t worry about any of the frequency stuff
If filing for 3+ turbines, you must add “Multiple Cases”
  Fill out OECaseDataSpreadsheet V2.0
  Due Diligence – Resources / Aviation (there’s also a link on the website)

## Slide 36: Notice of proposed Construction
Adding Multiple Cases

## Slide 37: Notice of Proposed Construction
Add due date into the project in Taskworld
When that due date gets close, check the FAA’s portal regularly
When a determination has been made they will email filings@oneenergyllc.com
Check off task in Taskworld
READ THE DETERMINATION … EVERY WORD OF IT
Notify all people involved the results of the determination
Next Steps

## Slide 38: 7460-2
Within 5 days of the turbine reaching its max height we have to file the 7460-2 with the FAA
If the turbine as-built location is within 1 arc second of the filed location and overall height of the turbine has not increased:
  Input as-built turbine locations and ground elevation
  Attach site drawing with coordinates
If the turbine as-built location is outside 1 arc second or total height has increased:
  FAA will prompt you to refile the structure
  (this is NOT what we want)
Keep tabs on when turbine lat/lons have changed and how they compare to the coordinates we filed with the FAA
If turbine siting changes, update the FAA filing prior to the 7460-2
Check off task on project master in Taskworld
After Turbine is Built

## Slide 39: Questions?
Questions? Comments? Concerns?
Turbine Suitability
Next class: