## Slide 1: PPT Wind school (class 17) Turbine suitability

## Slide 2: outline
Introduction
Goldwind forms overview
How to fill out
Sending to Goldwind

## Slide 3: introduction
Turbines are not one-size fits all
Need the right turbine for the wind regime
IEC 61400-1
Designed for specific conditions, including average wind speed and turbulence
Roman numeral is for average wind speed
  I is the highest wind speed class, III is the lowest wind speed
Letter is for turbulence
  A is highest turbulence intensity, C is the lowest turbulence intensity

## Slide 4: Goldwind forms overview
Templates:
Due Diligence - Working\Templates\GW Forms
Form for Turbine Selection
Load Calc App
Site Conditions

## Slide 5: Goldwind forms overview
Form for Turbine Selection
Load Calc App
Site Conditions
All these forms contain variants of the same information that are necessary for Goldwind to run their internal models and determine which class of turbine should be used for the project.

## Slide 6: Goldwind forms overview
Proposed Suitability Form
We’ve been going back and forth with GW on what information is necessary to provide for turbine suitability. We sent comments to GW on their proposed
It’s likely that the rest of this presentation will be null shortly and we will move towards this form.
In the meantime…

## Slide 7: Goldwind forms overview
Form for Turbine Selection
Environmental Conditions
Site Conditions
GW-portion to fill out
TI by ws and Wohler exponent
WS distribution
Project Info

## Slide 8: Goldwind forms overview
Load Calc App
Environmental Conditions
Site Conditions
GW-portion to fill out
Project Info
Yes, it’s in Chinese.
But we also have some translations in it to make it easier to know what they are asking for.

## Slide 9: Goldwind forms overview
Site Conditions
Turbine Locations
Weibull parameters
Average WS
Site air density
Inflow angles
Winds

## Slide 10: Goldwind forms overview
Site Conditions
Effective TI by wind speed with varying Wohler exponents, for all directions.
TIamb is Ambient TI
Pw,avg is average probability of wake for all turbines
Pwki is the probability of wake at turbine i in directional sector k
N is number of neighboring turbines
m is Wohler exponent
j is number of turbines
k is directional sector
TIwake is wake-induced TI
Effective TI is the turbulence intensity that takes the wakes of neighboring turbines into consideration and accounts for the added turbulence intensity.

## Slide 11: How to fill out
Intro
OH WAIT. WE DID!
And we even formatted the WRA to be in line with the GW form.
Thanks Past-PPT team. You really thought about Future-PPT team.
If only we had crunched these numbers beforehand during the WRA since we were working with all that data anyways…
All information in these forms must be exact to the WRA.
At this point in the DE process, the WRA is likely already reviewed and signed by IE so we MUST USE THE VALUES FROM IT

## Slide 12: How to fill out
Form for Turbine Selection
Basic project information
WRA:
Section 6. Environmental Conditions
Subparts A-C, E-G
A
A
A
B
C
C
E
E
F
G

## Slide 13: How to fill out
Form for Turbine Selection
WRA:
Section 6. Environmental Conditions
Subpart D
Section 7. Site Conditions
Subparts A, B, D, E, G
Section 2. Project and Site Info
Subpart A
6D
7A
7B
7B
7B
7B
7E
7E
7E
7D
7A
2A
7G
7G
Always 0.11

## Slide 14: How to fill out
Form for Turbine Selection
WRA:
Section 7. Site Conditions
Subpart E
7E
Need to create distribution based on MCP’d dataset used for Weibull calcs
Need to make figure for each report

## Slide 15: How to fill out
Load Calc App
Project name. Confirm it’s the same as the Form for Turbine Selection
WRA:
Section 6. Environmental Conditions
Subparts A-C, E-G
Make sure you’re answering the right questions. Look at previous GW forms if you are unsure what exactly is being asked.

## Slide 16: How to fill out
Load Calc App
WRA:
Section 6. Environmental Conditions
Subpart D
Section 7. Site Conditions
Subparts A, B, D, E, G
Section 2. Project and Site Info
Subpart A
(1) Average, all direction TI in %
(2) TI at 15 m/s in %; Standard dev of TI at 15 m/s in %
(3) Rep-TI at 15 m/s in %
P50 wind shear α all WS > cut-in
Always 0.11

## Slide 17: How to fill out
Site Conditions
Need to put turbine lat/lons into Universal Transverse Mercator (UTM) coordinates
WRA:
Section 6. Site Conditions
Subpart A
*all turbines use same values
WRA:
Section 7. Environ’l Conditions
Subpart D
*all turbines use same values
WRA:
Section 7. Environ’l Conditions
Subpart D
*each turbine is different value, then max/min is of all the turbines
*AB is max inflow angle
WRA:
Section 7. Site Conditions
Subpart D; P50 all ws > cut-in
*all values are the same
WRA:
Section 7. Site Conditions
Subpart B; 50 yr extremes
*all values are the same

## Slide 18: How to fill out
Site Conditions
WRA:
Section 7. Environ’l Conditions
Subpart E
*Effective TI by turbine and by Wohler exponent

## Slide 19: sending to goldwind
Process
Complete all three files and PDF
Signed off by another person
Let Head of PPT know GW files are complete
HoPPT will send forms to GW-US
GW-US will send to GW-C
GW-C uses all the information to run loads modeling
GW-C sends loads report back to GW-US
GW-US sends HoPPT loads report
HoPPT sends loads report to Construction
Construction then sends to Nester for tower analysis
Discussions with GW-C/GW-US regarding results of loads report
Approval for type of turbine for project

## Slide 20: sending to goldwind
Process
Complete all three files and PDF
Signed off by another person
Let Head of PPT know GW files are complete
We do NOT use GW as an editor.
We need to triple check each form sent to them for correct numbers and typos.
Things to do:
Confirm all values with the WRA
Confirm spelling of project names, project location, lat/lons
Have a second person confirm and approve all values/words as well
CHECK TO SEE IF GW WAS SENT A FORM ALREADY FOR A NEARBY PROJECT
If GW form was already sent for a nearby project, compare values for current project with the other project. Make sure they are comparable and not drastically different.

## Slide 21: sending to goldwind
Process
HoPPT will send forms to GW-US

## Slide 22: sending to goldwind
Process
HoPPT will send forms to GW-US
GW-US sends to GW-C

## Slide 23: sending to goldwind
Process
HoPPT will send forms to GW-US
GW-US sends to GW-C
GW-C uses information to run loads models

## Slide 24: sending to goldwind
Process
HoPPT will send forms to GW-US
GW-US sends to GW-C
GW-C uses information to run loads models. Creates loads report

## Slide 25: sending to goldwind
Process
HoPPT will send forms to GW-US
GW-US sends to GW-C
GW-C sends loads report to GW-US
GW-C uses information to run loads models. Creates loads report

## Slide 26: sending to goldwind
Process
HoPPT will send forms to GW-US
GW-US sends to GW-C
GW-C sends loads report to GW-US
GW-US sends loads report to HoPPT
GW-C uses information to run loads models. Creates loads report
All of these steps combined are contractually supposed to take 21 days.

## Slide 27: sending to goldwind
Process
Discussions with GW-C/GW-US regarding results of loads report
Approval for type of turbine for project
Sorry, but according to these values you provided, the turbine you want failed at 23 m/s for TI and loading.
We can mitigate that! We will turn the turbines off at 20 m/s regardless so it will not be affected.
Sounds good to me!
You may have a turbine.

## Slide 28: sending to goldwind
Process
HoPPT sends loads report to Construction
Construction then sends to Nester for tower analysis

## Slide 29: sending to goldwind
Process
HoPPT sends loads report to Construction
Construction then sends to Nester for tower analysis

## Slide 30: sending to goldwind
Process
HoPPT sends loads report to Construction
Construction then sends to Nester for tower analysis
PPT’s work here is done.

## Slide 31: homework
Read Chapter 6 (External Conditions) of IEC 61400-1
Due next class

## Slide 32: Questions?
Questions? Comments? Concerns?
Next Steps Part 1
Next class: