## Slide 1
Electricity 101
Michelle kleinau
8/3/2021
*Slides adapted from original electricity 101 presentation by john everett

## Slide 2: Outline
Alternating Current (AC)
3 Phase AC power
Transformers
One Line Diagram
In Operation

## Slide 3: Electricity
Electrons move from atom to atom
Voltage: electrical “pressure” or “potential” or “potential difference”
  Units: Volts (V)
Current: flow of electrons (I)
  Units: Amperes or Amps (A)
Notes: Voltage: pressure of water in a pipe
Current: flow of water
If pipe is sealed, pressure but no current

## Slide 4: “Power Wheel”
Notes: Won’t discuss resistance

## Slide 5: AC vs. DC

## Slide 6: War of Currents
Direct Current (DC)
  Thomas Edison
  Low voltage (~100 Volts) systems
  Distributed generation
Alternating Current (AC)
  Nikola Tesla and George Westinghouse
  Allows high voltage generation
  Easy conversion from higher-to-lower and lower-to-higher voltage with transformer
  Transmission much more efficient
Late 1800s
Notes: 2 schools of thought when electricity was invented
AC won out

## Slide 7: Outline
Alternating Current (AC)
3 Phase AC power
Transformers
One Line Diagram

## Slide 8
Notes: Draw picture showing moving vertically vs. horizontally through field

## Slide 9
Notes: Current moving in different direction in 2 wires, but connected in loop

## Slide 11: AC Single phase (1Φ)
Frequency = 60 Hertz (Hz) = 60 cycles per second
Notes: Frequency!

## Slide 12: AC Voltage
Voltage:
  Electrical “pressure” or “potential difference”
Which way do electrons want to flow?

## Slide 13: AC Voltage
Voltage:
  Electrical “pressure” or “potential difference”
Which way do electrons want to flow?
Higher voltage to lower voltage

## Slide 14: AC Single phase (1Φ)
Line-Ground
Frequency = 60 Hertz (Hz) = 60 cycles per second
Notes: 0=ground

## Slide 15: Outline
Alternating Current (AC)
3 Phase AC power
Transformers
One Line Diagram

## Slide 18: Three Phase (3Φ ) AC Voltage
Voltage:
  Electrical “pressure” or “potential difference”
Which way do electrons want to flow?

## Slide 19: Three Phase (3Φ ) AC Voltage
Voltage:
  Electrical “pressure” or “potential difference”
Which way do electrons want to flow?
Higher voltage to lower voltage

## Slide 21
Line-Line (Phase-Phase) = * Line-Ground
A
B
A-B

## Slide 22
What’s the big deal? Why Three Phase?
Notes: P=IV

## Slide 23
Single Phase
Power (Watts) = Volts * Amps
Notes: Power is always positive here!

## Slide 24
Notes: Light bulb will flicker

## Slide 25
Power in each Phase varies, but
Total Power is CONSTANT
A
C
B
Total Power
Notes: Add all 3 phases (power) together

## Slide 26: Three Phase (3Φ ) AC
Three separate conductors, each with Voltage and Current shifted 120° relative to each other
Voltage
  Line-Ground
  Line-Line (Phase-Phase) = * Line-Ground
Current
  Current in each phase = total current /
Power = V * A
  Power in each phase varies
  Total power is constant
Summary

## Slide 27: Three Phase (3Φ ) AC
Total power is constant
With one additional conductor (3 vs. 2) increase power x 3
Easy conversion from higher-to-lower and lower-to-higher voltage with transformer
Allows high voltage generation
Transmission much more efficient
Advantages

## Slide 28: Outline
Alternating Current (AC)
3 Phase AC power
Transformers
One Line Diagram

## Slide 30: Transformers

## Slide 31: Transformers
E2 / E1 = N2 / N1
or E2 = E1*N2 / N1
If E1=4160V; N2=100; N1=1733; I1=15A
Find E2:
E2 = 4160V*100/1733 = 240V

## Slide 32: Transformers
Also
I2 / I1 = N1 / N2
or I2 = I1*N1 / N2
Find I2:
I2 = 15A *1733/100 = 260A

## Slide 33: Transformers
Find Power = V*A = Watts
P1 = 4160V * 15A = 62,400 Watts
P2 = 240V * 260A = 62,400 Watts

## Slide 34: Step down transformer
1Φ

## Slide 35: Voltage
Line-to-Line = 4160V
Why 4160V? Line-to-ground = ?

## Slide 36: Voltage
  Line-Line = * Line-Ground
therefore
  Line-Ground = Line-Line /
Line-Ground = 4160V /
= 2400V

## Slide 37
 | Line-to-Line | Line-to-Ground
Lafarge, Harpster | 4160 | 2400
WP Findlay, WP Ottawa, WP Greenville, Haviland, Cooper Farms | 12470 | 7200
Ball (1+2), Valfilm, WP Marion | 34500 | 20000
Project Voltage

## Slide 38: Step down transformer
3Φ

## Slide 39
Transformer Connections
(Wye)

## Slide 40
Delta
Less Costly
Filter Harmonics
Operate with One Ground Fault
Protection More Complex
Star (Wye)
More Costly
Easier Protection
Safer
Transformer Connections

## Slide 41: Step Up Transformer
Same power in primary and secondary windings (except very small losses)
Why step up voltage?
  Power loss α I2 (I = current) higher volts → lower amps → lower power loss
  Conductor size based on amps lower amps → smaller conductor → lower cost
Why?

## Slide 47: Outline
Alternating Current (AC)
3 Phase AC power
Transformers
One Line Diagram

## Slide 48: One Line Diagram
Whirlpool Greenville

## Slide 49: One Line Diagram

## Slide 50: One Line Diagram
Power (per Phase)
12470kV x 70A / √3 = 500kW
600V x 1430A / √3 = 500kW
(4) 500 MCM CU
(1) 4/0 AL
Step Up Transformer:
600V to 12470V
Low = Wye (Star)
High = Delta

## Slide 51: One Line Diagram
Switchgear

## Slide 52: One Line Diagram
Switchgear

## Slide 53: Switchgear

## Slide 54: In Operation
Whirlpool Findlay
From Turbine(s)
To Plant
To Switching Station

## Slide 55
Questions?

## Slide 56: Transformers