## Slide 1: Electric utilities
FE/PE seminar | Feb 11 2019 | Erin Roekle

## Slide 2: outline
Introduction
Background
Electricity Utilities in OH
Billing Basics
IOU Billing (OH)
Co-Op/Muni Billing (OH)
OE-specific Billing Notes
Real-Life Super Fun Note

## Slide 3: introduction
So so sorry.
Utilities are wonky and each do things slightly differently. There isn’t a one-size-fits-all explanation for utilities.
We’re about to get into the weeds on this and there is a bunch of background knowledge that is necessary to see how everything fits together. I’m sorry in advance.

## Slide 4: background
Power/Energy Basics
We’re all engineers.
We should know the difference between power and energy.
POWER
ENERGY
RATE at which work is done
Capacity to do work
No, they are not interchangeable. Let’s all use the correct terminology.

## Slide 5: Background
Power/Energy Basics

## Slide 6: Background
Power/Energy Basics
Apparent (VA)
Real (W)
Reactive (VAR)
Phase Angle ()
Real (W): Real power which is dissipated in the circuit
(useful power)
Apparent (VA): Total power
Reactive (VAR): Doesn’t do any useful work on the load (useless power)
Indicator of machine efficiency
Indicator of load consistency

## Slide 7: Background
Grid Structure
Independent System Operator (ISO) / Regional Transmission Organization (RTO)
Electricity Distribution Utility (EDU)
End-User
Pricing Node (PNode)
End-Users’ Meter

## Slide 8: Background
Grid Structure Cont’d
Independent System Operator (ISO) / Regional Transmission Organization (RTO)
Transmission system operator that coordinates, controls, and monitors a multi-state electric grid; administers region’s wholesale markets
Regulated by FERC (national jurisdiction)
Developed out of the concept of grid reliability
Very subtle difference between the two – typically ISOs are within a single state and RTOs are multi-state; RTOs have added component of more responsibility for transmission network

## Slide 9: Background
Grid Structure Cont’d
Electricity Distribution Utility (EDU)
Distribution system operator that purchases energy commodity from the wholesale market and distributes to end-users at retail rates
The “wires and infrastructure group” that get the energy commodity from nodes/hubs to the end-user
Who you typically see an electricity bill from

## Slide 10: Background
Grid Structure Cont’d
Pricing Node (PNode)
Specific electrical bus location where settlement prices are determined
Settlement prices/market-clearing price is called Locational Marginal Price (LMP)
Can think of LMP as the wholesale cost for the commodity of energy at specific time in a specific market
Settlement prices vary based on what part of the electric market you’re playing in
Day-Ahead; Hour-Ahead; 15-Min-Ahead; Real-Time; etc

## Slide 11: Background
Grid Structure Cont’d
End-Users’ Meter
Device that measures that amount of energy consumed by the end-user
Running total of kWh consumed
Continuously measuring the instantaneous voltage and current to determine energy that flows through it

## Slide 12: background
Regulated vs Deregulated
REGULATED
DEREGULATED
Utilities own and operate all electricity
Utilities control everything from generation to end-user meter; utility owns the infrastructure and lines and sells directly to end-user
Utilities have to abide by rates set by the state public utility commissions

## Slide 13: background
Regulated vs Deregulated
REGULATED
DEREGULATED
Utilities own and operate all electricity
Utilities controls everything from generation to end-user meter; utility owns the infrastructure and lines and sells directly to end-user
Utilities have to abide by rates set by the state public utility commissions
Competitors can enter market to invest in power plants and lines
Generation owners can sell wholesale electricity to retail suppliers, who then can sell at retail prices to end-users
Gives customers options to chose their energy commodity supplier; still have utility distribution costs

## Slide 14: background
Regulated vs Deregulated
REGULATED
DEREGULATED
Utilities own and operate all electricity
Utilities controls everything from generation to end-user meter; utility owns the infrastructure and lines and sells directly to end-user
Utilities have to abide by rates set by the state public utility commissions
Competitors can enter market to invest in power plants and lines
Generation owners can sell wholesale electricity to retail suppliers, who then can sell at retail prices to end-users
Gives customers options to chose their energy commodity supplier; still have utility distribution costs

## Slide 15: background
Regulated vs Deregulated Cont’d
Gas + Electricity Deregulated
What does that mean for me?
You have the opportunity to “shop” for the energy and gas commodity, but the utilities will still charge you to get the commodity to you
Can still get energy and gas commodity through the utility, but it’s the idea of having the choice to pick where you get that commodity

## Slide 16: Electric utilities (OH)
Municipalities
Public Utilities/
Co-Operatives
Notes: How are the lines defined?

## Slide 17: Electric utilities (OH)
CERTIFIED TERRITORY ACT (ORC 4933.81-90)
Essentially, what this Act does is:
Draws boundaries within the state to allow for a single EDU to distribute electricity within said boundaries
Katie is likely going to go more in-depth

## Slide 18: Electric utilities (OH)
Public Utilities vs Muni vs Co-Op
PUBLIC UTILITY (IOUs)
CO-OPERATIVE
Investor-owned utility – owned by stockholders
Owned by its members (members are end-users)
Non-profit, cost-of-service basis
Stockholders do not have to be end-users
For-profit
MUNICIPALITY
Owned by city/state/federal government
Only applicable to the specific jurisdiction of the municipality
Regulated by PUCO
Regulated by members and board
Regulated by governing body (city council, etc)

## Slide 19: Billing basics
Components of a Bill
TOTAL BILL
ENERGY COMMODITY
(GENERATION)
TRANSMISSION
DISTRIBUTION
ADMINISTRATIVE/RECOVERY

## Slide 20: Billing basics
Components of a Bill Cont’d
TOTAL BILL
FLAT COSTS
kWh-BASED COSTS
kW-BASED COSTS
kVA-BASED COSTS
COMBO-BASED COSTS

## Slide 21: Billing basics
Components of a Bill Cont’d
ENERGY COMMODITY
(GENERATION)
TRANSMISSION
DISTRIBUTION
ADMINISTRATIVE/RECOVERY
FLAT COSTS
kWh-BASED COSTS
kW-BASED COSTS
kVA-BASED COSTS
COMBO-BASED COSTS

## Slide 22: Billing basics
Rate Schedules
RATE SCHEDULE (TARIFF):
Document that lists the various types and amounts of charges or line items that can be made to customers in a particular rate class
The “extras” other than generation and demand charges are called RIDERS
Each rider recovers costs for a particular reason that is laid out within the rate schedule. Money brought in from that rider must be used for that purpose only
RIDER A
RIDER F
RIDER B
RIDER D
RIDER C
RIDER N
Rate class is dependent on two main things:
1) Demand needs; 2) Voltage for receiving
Rider rates vary based on rate schedule
Billing Demand and Consumption value used as values for riders
RATE SCHEDULE 1

## Slide 23: Billing basics
DEMAND
CONSUME
Rate Schedules Cont’d
Typically, the 15-min peak kW value within the billing period
DEMAND VALUE
CONSUMPTION VALUE
RIDER A
RIDER F
RIDER B
RIDER D
RIDER C
RIDER N
RATE SCHEDULE 1
Chart: 15-min Interval Demand
In addition to the riders, there are demand charges and consumption charges
PK kW: 2120
Total kWh consumed during billing period
Chart: 15-min Interval Demand
INTEGRAL OF INTERVAL DATA
kWh: 1150000

## Slide 24: IOU billing (OH)
DUKE ENERGY
AEP
FIRST ENERGY
DP&L

## Slide 25: IOU billing (OH)
ESPs
ELECTRIC SECURITY PLAN (ESP):
A rate plan for the supply and pricing of electric generation service.
Requires IOU to offer a Standard Service Offer (SSO) for customers who do not actively shop for generation
SB 221 (2008)
IOU can decide between filing an ESP or a Market Rate Offer (MRO) with PUCO
IOU cannot own generation entities and must be distribution entity only
ESPs are traditional rate plans that require the utility to get all its energy capacity for its SSO customers through wholesale auctions, auction prices determine generation rates
Must be approved by PUCO
Defines what riders are going to be active during this ESP
Currently, all public utilities only file ESPs
ESPs last 3-5 years

## Slide 26: IOU billing (OH)
SSO
Rate Schedule number coincides with SSO
But what is SSO?
End-user purchases generation through the utility, as well as the transport of the generation to its facility; utility does everything
One electricity bill per month
(assuming one meter)
Demand Charges + Riders Cost (Getting it to You + Extras)
Generation Costs (Energy Commodity)
Billing Values

## Slide 27: IOU billing (OH)
Shopping
Rate Schedule number coincides with SHOPPING
But what is SHOPPING?
End-user purchases generation through a third-party (Certified Retail Electricity Supplier – CRES); utility gets energy commodity to end-user
Typically two electricity bills per month; one from the utility and the other from the CRES
(assuming one meter). Sometimes combined billing for only one bill
Demand Charges + Riders (Getting it to You + Extras)
Billing Values

## Slide 28
Demand Charges + Riders (Getting it to You + Extras)
Billing Values
Generation Costs (Energy Commodity)

## Slide 29: muni billing (OH)
Billing Values
Generation Costs (Energy Commodity)
Demand Charges + Riders (Getting it to You + Extras)
End-user has no choice in where it gets generation from; Muni gets to pick
The majority of the Munis get their generation through the broker American Municipal Power (AMP)

## Slide 30: Co-op billing (OH)
Billing Values
Generation Costs (Energy Commodity)
Demand Charges + Riders (Getting it to You + Extras)
End-user has no choice in where it gets generation from; Co-Op gets to pick
The majority of the Co-Ops get their generation through the broker Buckeye Power

## Slide 31: TAX billing (OH)
Ohio General Assembly created a kWh tax in 2001
Tiered rate structure based on end-users consumption per billing period; not rate class specific
EDU is responsible for collecting the tax and providing to the OH Dept of Taxation
Mega-users can SELF ASSESS if annual consumption is greater than 45 million kWh per year – lots of paperwork is involved
0-2,000 kWh
2,001-15,000 kWh
15,001+ kWh
$0.00465/kWh
$0.00419/kWh
$0.00363/kWh
0-500 mil kWh
$0.00257/kWh
500 mil+ kWh
$0.00183/kWh
*Billed monthly, metered ANNUALLY
*Billed monthly, metered MONTHLY
Katie is likely going to go more in-depth

## Slide 32: Oe-specific billing notes
Net-Metering
NET-METERING:
A billing mechanism to allow for crediting of behind-the-meter generation. Based on billed values at end of billing period, takes time element out. Offsets retail rates. In OH, only IOU’s are required to allow for net-metering. Co-Ops and Munis have the option to allow it, but most do not.
GRID
Month Need: 1,000,000 kWh
Month Production: 200,000 kWh
NET to Facility: 200,000 kWh
NET to Grid: 0 kWh
NET from Wind: 200,000 kWh
NET from Grid: 800,000 kWh
200,000 kWh
800,000 kWh
0 kWh
NET to Facility: 800,000 kWh
NET from Wind: 0 kWh
MONTH NET CONSUMER
Utility bills the consumption value as the NET kWh from the grid to the facility (800,000 kWh in this example) and the billing demand still is considered the peak 15-min kW

## Slide 33: Oe-specific billing notes
Net-Metering
GRID
Month Need: 1,000,000 kWh
Month Production: 1,300,000 kWh
NET to Facility: 1,000,000 kWh
NET to Grid: 300,000 kWh
NET from Wind: 1,000,000 kWh
NET from Grid: 0 kWh
1,000,000 kWh
0 kWh
300,000 kWh
NET to Facility: 0 kWh
NET from Wind: 300,000 kWh
MONTH NET PRODUCER
Utility bills the consumption value as the NET kWh from the grid to the facility, if negative then NET kWh is 0 kWh (0 kWh in this example) and the billing demand still is considered the peak 15-min kW
NET-METERING:
A billing mechanism to allow for crediting of behind-the-meter generation. Based on billed values at end of billing period, takes time element out. Offsets retail rates. In OH, only IOU’s are required to allow for net-metering. Co-Ops and Munis have the option to allow it, but most do not.

## Slide 34: Oe-specific billing notes
Using PURPA/Avoided Costs
QUALIFYING FACILITY (QF):
Federal PURPA gives everyone opportunity to interconnect to offset their load. Excess energy from the Qualifying Facility (behind-the-meter generation entity) sold in real-time and compensated at Avoided Cost. We use this in Co-Op and Muni territories.
Katie is likely going to go more in-depth
Avoided Costs are similar to Wholesale Rates.
For any power sent back to the grid, only compensated at wholesale. Not as financially advantageous as net-metering.
Biggest thing this means is we have to size projects appropriately to minimize the amount of power sent back.

## Slide 35: Real-life fun note
City of Findlay Government Aggregate = good thing

## Slide 36: Questions?
Questions? Comments? Concerns?