## Slide 1: Parts of the Substation
Over Head Structures
Station Post Insulators
89L
Disconnect Switch
52L
Breaker
(Line/Bus Protection)
CTPTs
Surge Arresters
52T
Breaker
(Transformer protection)
Main Power Transformer
Oil Containment
Junction
Box
Static
Pole (Shield Mast)
Control
House
Dead End Pole (Interconnect)
Ballistic Wall

## Slide 2: North View

## Slide 3: Bird’s eye View

## Slide 4: Zones
SAFETY ZONE
HAZARD ZONE
KNOX LOCK

## Slide 5: Zones
SAFETY ZONE
HAZARD ZONE

## Slide 6: The control house

## Slide 7: Control Enclosure
Bullet Proof Glass
  Windows aren’t typical for substations
High Strength Precast Concrete Structure
Contains Electrical systems
  Breaker and Fiber Enclosure “Big Ass Box”
  Relay Racks
  Battery Backup and Chargers
Controls all 240/120 VAC and 125VDC systems
  Lights
  Future Cameras
  Equipment Control Power
  Internal Accessories

## Slide 8: Control House interior

## Slide 9: The Control House

## Slide 10: ‘Big Ass Box’
Controls house and yard’s ancillary equipment
Connection point for equipment low voltage supply
Fiber Junction connecting Equipment to Relays

## Slide 11: Equipment Feed Lines
2 Cables brought into each piece of equipment
Industry practice involves many more cables and prevents quick swapping/wiring of equipment.
OE practice allows quicker installs, easier wiring
Plug n’ Play

## Slide 12: How our cables travel
Control
138kV
34.5kV
19.9kV

## Slide 13: Redundancy of CONTROL power 1
138kV enters Hub
Converted to 34.5kV at Main Power Transformer
Converted to 120/240V at pad mount.

## Slide 14: Redundancy of CONTROL power 2
Following Loss of Sub Main Power (grid)
Propane Generator automatically kicks on.
Feeds 120/240V to power Control Enclosure

## Slide 15: Redundancy of CONTROL power 3
Following Loss of Sub Main Power (grid) and Propane Generator
Also, holdover power between transitions
125VDC (60 Cells) Lead Acid Battery

## Slide 16: The Relay racks
CONTROL
MAIN BUS
MERCURY
FEEDERS

## Slide 17: Relays overview
CTVT
MPT1
52T1
52L
89L
87T1
SEL 487E
11L
SEL 451
87B-A
SEL 487B
RTAC
SEL 3530

## Slide 18: 11L SEL 451
CTVT
52L
89L
11L
SEL 451
OPEN CLOSE
VOLTAGE
METERING DATA
CURRENT
TRIP COIL

## Slide 19: 87B-A SEL-487B
52T1
52L
87B-A
SEL 487B
OPEN CLOSE
VOLTAGE
METERING DATA
CURRENT
TRIP COIL
CTVT

## Slide 20: 87T1 SEL 487E
MPT1
52T1
87T1
SEL 487E
OPEN CLOSE
VOLTAGE
METERING DATA
CURRENT
TRIP COIL

## Slide 21: RTAC SEL 3530
CTVT
RTAC
SEL 3530
OPEN CLOSE
VOLTAGE
METERING DATA
CURRENT
TRIP COIL
SWITCHGEAR:
SEL735
SEL351

## Slide 24: Questions so far?

## Slide 25: Thank you for your time