## Slide 1
One Energy Operations
Erica Johnson
6/8/2021

## Slide 2: Overview
Operations
  Turbine Info
  Project Info
  Service Schedules
  SOPs
  Production Reports
System Operations
  Overview
Safety & Quality
  NCRs
  Mistakes & Mishaps
  Training
Future Functions

## Slide 3: Turbine Info
Goldwind 1.5 MW Permanent Magnet Direct Drive
  Full power conversion
  Generator driven by rotor

## Slide 4: Project Info
NUMBER | PROJECT | LOCATION | SIZE | YEAR INSTALLED | DELIVERY METHOD
S014 | Haviland Plastics | Haviland, OH | 4.5 MW | 2012 | CAPEX
S015 | Cooper Farms | Van Wert, OH | 4.5 MW | 2011/2012 | CAPEX
S017 | MPC Harpster | Harpster, OH | 1.5 MW | 2016 | REA
S019 | Zephyr 1.0 | Findlay, OH | 4.5 MW | 2016 | REA
S020 | Whirlpool Findlay | Findlay, OH | 3.0 MW | 2016 | REA
S023 | Whirlpool Marion | Marion, OH | 4.5 MW | 2017 | REA
S024 | Whirlpool Ottawa | Ottawa, OH | 1.5 MW | 2018 | REA
S025 | Valfilm | Findlay, OH | 3.0 MW | 2018 | REA
S026 | Whirlpool Greenville | Greenville, OH | 4.5 MW | 2018 | REA
S027 | Autoliv | Findlay, OH | N/A | N/A | N/A
S028 | LafargeHolcim | Paulding, OH | 4.5 MW | 2020 | REA
S030 | Zephyr 2.0 | Findlay, OH | 4.5 MW | 2020 | REA

## Slide 5: Service Schedules
Performed semi-annually, both OE and Goldwind at REA projects
OE not responsible for maintenance at CAPEX projects; audit climbs and blade inspections only

## Slide 6: Goldwind Maintenance
500 Hour Maintenance
  Detailed maintenance on systems including converter, yaw, pitch, cooling, heating, auto lubrication
Semi-Annual Maintenance
  Component inspection, bearings greased, visual inspection of bolted connections, function test turbine auxiliary systems
Annual Maintenance
  10% check of bolted connections, general inspection, bearings greased, function test cooling/heating systems, yaw system test, generator test

## Slide 7: One Energy Maintenance
Anchor bolt 10% tensioning
  3 months, 6 months, yearly thereafter
  10% of bolts are tensioned to verify tightness
Semiannual Inspection
  Quality control inspection – full turbine system, BOP equipment, project site
Annual Inspection
  Quality control inspection – full turbine system, BOP equipment, project site
  Detailed BOP inspection – electrical and CEE
Blade Inspections
  Semiannual drone inspection of blades, root to tip
  Goal is quarterly inspections

## Slide 8: One Energy Maintenance

## Slide 9: Maintenance Documentation
One Energy
  Completed checklists are used to compile punchlists for OE and OEM
  PDF’d Reports – Dropbox\Projects Operating\[Project]\Maintenance & Inspection
  Inspection photos – saved in NoteVault
  Blade Inspection photos – saved in Photos – Project Specific
  Completed reports are uploaded to Fixx
OEM
  Reports uploaded to DataRoom by the OEM

## Slide 10: Standard Operating Procedures (SOPs)
Still in progress
Safety/LOTO
  Turbine Operation
  Turbine Rotor
  Project Primary Feed Switchgear LOTO
  Turbine Pad-Mount LOTO
Turbine Maintenance
  Anchor Bolt Tensioning
  Tower Torquing
  Nacelle Torquing
  Generator Torquing
  Rotor Torquing
  Generator Insulation Testing
  Turbine Emergency Pitch System 90° Test
  Overtwist Protection System Test
  Pitch System Capacitor Emergency Pitch Test
  Checking Blade 0 Procedure
  Mechanically Locking Blade
  Replacing Pitch Belt
Blade Maintenance
  Aerial Drone Inspection
  Rope Access Inspection/Repairs
  Platform Access Inspection Repairs
Balance of Plant (BOP) Equipment Maintenance
  Transformer Oil Sampling

## Slide 11: Production Reports
Monthly
  Sent to customer, uploaded to Athena & MyWindProject
  Production, downtime, availability, metering info (if applicable)
  SCADA Data + metering sheet

## Slide 12: Production Reports
Monthly Goldwind Report
  PDF report and Excel availability tracker
  PDF uploaded to Athena
  SCADA Data

## Slide 13: Production Reports
Quarterly Report
  Prepared for Fleet Alpha (Rosemawr) each quarter
  Multiple components: Legal, Technical, Financial
  Operating project data used to create summary sheets
  Safety and insurance stats
  Monthly reports included

## Slide 14: Production Reports
OPAR
  Currently a PPT function
  Analyzes the first 14 months of operation of a project
  Uses SCADA data and MERRA2 data to determine wind performance
  Reforecasts the production estimate – Operating P50

## Slide 15: System Ops
Rotating teams – weekly rotation
Respond to grid events, weather events, comms, planned outages, etc.
More fun details at an SO training near you

## Slide 16: Safety & Quality
Accident/incident reporting
  NCRs
  M&Ms
Training

## Slide 17: NCRs
Created for quality issues that impact a project, whether construction or operation
Includes dates issue identified/corrected, parties responsible and involved, cost, analysis
Example: Rail bracket bolt repair

## Slide 18: Safety
Near Miss
  Something could have happened
Recordable
  OSHA definitions
M&Ms (Mishaps & Mistakes)

## Slide 19: Training
EMT/AEMT
Tower Rescue
Local Fire Department Training

## Slide 20: Future Ops functions
Meter reads
OPARs
Blade Inspections
System Ops
Planned outages
ManagedHV maintenance/inspection/operations